## Slide 1: Realizing VSF Mode
Alternatives within reach?

## Slide 2: Alternative to VSF Mode: VSF2
Use +-+- instead of gg+- to avoid needing a 3 output switch:
VSF
D
D
D
D
A
A′
A
A′
VSF2
D
D
D
D
E
E
E
E
VSF2.5
D
D
D
D
A
E
A
E
A | +-gg
D | ++gg
E | +-+-

## Slide 3: Alternative to VSF Mode: VSF2
Can look at the trap figure:
(VSF2)
(VSF2.5)

## Slide 4: Alternative to VSF Mode: VSF2
Can look at the trap figure:
SF
VSF
VSF2
VSF2.5
SF < VSF2 ~ VSF2.5 < VSF

## Slide 5: Alternative to VSF Mode: VSF2
We need simulation to see how close VSF2, VSF2.5 come to VSF:

## Slide 7: Alternative to VSF Mode: VSF2
We need simulation to see how close VSF2, VSF2.5 come to VSF.
Conclusion:
  VSF2.5 < SF < VSF2 < VSF
  VSF2 only 25% better than SF.
Why? Maybe the asymmetry of VSF2.5 increases ergodicity, more molecules escape than in SF, VSF.

## Slide 8: What about XSF?
Use ++-- instead of ++gg for even better focusing.
By simulation, wider phase space but not more density:

## Slide 10: What about XSF?
But the effective moving trap looks incredible:
S=1
SF
VSF
XSF
10 50 100 200 (mK)

## Slide 11: What about XSF?
Why the discrepancy?
  Low final speed. The XSF effective trap has a higher frequency, and thus requires more frequent focusing events to be realized.
If we compare at higher final speed:

## Slide 13: What about XSF?
Why the discrepancy?
  Low final speed. The XSF effective trap has a higher frequency, and thus requires more frequent focusing events to be realized.
If we compare at higher final speed:
  Now the transverse phase space looks more respectable.
  The gain shows no sudden dip near the end.
  We do need low speeds for trapping, but we should simulate trap-loading to decide, not simply ignore XSF because the phase space looks ugly.
Also, XSF2:

## Slide 14: XSF2
Like VSF2, we switch between only two states, ++-- and +-+-.
Can be achieved with two 30 kV push-pull switches.
  Or a 30 and a 20, running at +/-15kV and +/-10kV, which we have now
Unlike VSF2, it actually surpasses XSF slightly:
SF
VSF
VVSF
XSF2

## Slide 15: XSF2
Like VSF2, we switch between only two states, ++-- and +-+-.
Can be achieved with two 30 kV push-pull switches.
  Or a 30 and a 20, which we have now (!)
Unlike VSF2, it actually surpasses XSF slightly:
  Why? ++-- fields are strong enough to slow on their own, +-gg not needed.

## Slide 16: XSF2
Corroborate with Simulation:

## Slide 17
XSF XSF2

## Slide 18
XSF XSF2

## Slide 19
XSF XSF2

## Slide 20: XSF2
Corroborate with Simulation:
  Slightly worse than XSF, due to reduced Z-PSD.
  Stronger negative effect at the lowest speeds for XSF2 than XSF.
  Behaves worse than VSF with 8mm free flight to laser.
  Not necessarily worse for trap loading.
A hybrid setup for the last few stages?
  Could avoid defocusing +-+- configuration.
  Maybe ++-- is overfocusing at the lowest speeds.

## Slide 21: Alternative to VSF Mode: VSF2
BUT!
  Running XSF/XSF2 puts full voltage across adjacent pin pairs.
Maybe we can condition for this configuration…
-
+
+
-
-
+
+
-
Configuration +-+-

## Slide 22: Conditioning for XSF2 (+-+-/++--)
Surface Quality:
  Best side of pins are pointing towards each other.
  Worst parts are pointed away.
  Sides of pins are somewhere in between.
Spacing:
  Some inaccuracies in pin-pair spacing. Some may be as close as 1.5 mm to one another.
Overlap:
  Much smaller than normal configuration, by more than an order.
We could just try it.

## Slide 23: Electronic Requirements
To understand charge transfer we need a capacitance matrix:
Experiment (LCR SR720 Probe): COMSOL Simulation:
(pF) | Rod 1 | Rod 2 | Rod 3 | Rod 4 | GND
Rod 1 | 206 | -56 | -64.5 | -62 | -33
Rod 2 | -56 | 208 | -65 | -63 | -37
Rod 3 | 64.5 | -65 | 210 | -57 | -33.5
Rod 4 | -62 | -63 | -57 | 206 | -33.5
GND | -33 | -37 | -33.5 | -33.5 | 140
(pF) | Rod 1 | Rod 2 | Rod 3 | Rod 4 | GND
Rod 1 | 199 | -43 | -55 | -55 | -46
Rod 2 | -43 | 199 | -55 | -55 | -46
Rod 3 | -55 | -55 | 199 | -43 | -46
Rod 4 | -55 | -55 | -43 | 199 | -46
GND | -46 | -46 | -46 | -46 | 184

## Slide 24: Electronic Requirements
Using Capacitance Matrix, we can solve current during edges: